## Slide 1: Smart ROOM
S3-EE1953-Engineering design
Department of Electrical Engineering
University of Moratuwa
01

## Slide 2: Description of the project
In our project we have implemented a smart room using automatic lighting system with IOT based remote controlling.
When person enters the room, Bulb will turn on with the intensity of the light inside the room, And turn off when the person leaves the room or nobody inside the room.
We can also switch on the appliances inside the room through mobile or using any smart devices from anywhere.
03
 | Dark time | Day time
Person in room | Bulb on | Bulb off
No one in room | Bulb off | Bulb off

## Slide 3
Reason for our project:
Power saving by operating the bulbs and other appliances in efficient manner
Can control from anywhere in the world
Convenient use
04

## Slide 4
Sensors and other components
Ultrasonic distance sensor
LDR
Arduino Uno board
Wi-Fi module ESP8266(nodemcu)
Relay
05
Specification: HC-SR04

## Slide 5
Software used……
proteus
Arduino
06
Arduino iot cloud

## Slide 6
08
Ultrasonic sensor working principle

## Slide 7: LDR Sensor
It has a resistance that changes with light intensity that falls upon it.
=
=
We used R as 10KΩ in practical
=
0 < ADC value <1024
= ADC value * =ADC value *0.004828125
lux = = =
Resistance vs lux

## Slide 8
IOT Cloud Interface

## Slide 10
COMPONENTS | COST
2 Ultrasonic distance sensor | Rs 360.00×2 =720.00
1 LDR | Rs100.00
1 Arduino Uno | Rs 2000.00
Nodemcu | Rs 900.00
1 Relay | Rs 800.00
3 Bulb | Rs 170.00 3= 510.00
Total | RS 5030.00
COMPONENTS | COST
2 Ultrasonic distance sensor | Rs 360.00×2 =720.00
1 LDR | Rs100.00
1 Arduino Uno | Rs 2000.00
Nodemcu | Rs 900.00
1 Relay | Rs 800.00
3 Bulb | 
Total | RS 5030.00
Budget
09

## Slide 11
Group members
Subaraj .B 190605T
Laksman .P 190347D
Jalini .S 190246R
Kirushan .T 190318P
11

## Slide 12
THANK YOU!